## Slide 1
Simplify surface
Rebuild a heavy face as a lighter cubic B-spline within a tolerance -- or replace it in place.
gordonSurface · Onshape custom feature
Draft 2026-09-26

## Slide 2
What it does
Simplify surface · gordonSurface
Draft 2026-09-26
Imported, derived and fitted faces carry far more control points than their shape needs, which slows and destabilises later features. Simplify surface finds, curve by curve, the fewest control points within your tolerance.
Use it when
A heavy imported or fitted face
Downstream features are slow or fail on a face
Replace a face with a lighter one in place
Station curves are reduced, made compatible and skinned.

## Slide 3
The dialog
Simplify surface · gordonSurface
Draft 2026-09-26
IMAGE MISSING: docs/decks/simplify_surface/shots/dialog.png
# | Parameter | What it means
1 | Face | The face to simplify.
2 | Tolerance | 0.01-100 mm (1 mm).
3 | Continuity | G0 / G1 / G2 end derivatives along v (G2 mode has no effect).
4 | Mode | AUTO (Greville stations, binary search per curve) / MANUAL (U, V counts).
5 | Replace face | Replace the source face instead of a new sheet.
6 | Debug print | Console.

## Slide 4
Outputs and messages
Simplify surface · gordonSurface
Draft 2026-09-26
Outputs
Key | What it holds
simplified | The new sheet (or the replaced face).
Messages
 | Message / what to do
(none) | 

## Slide 5
Tips and limits
Simplify surface · gordonSurface
Draft 2026-09-26
!
Checked on stations
The error is measured along the station curves only.
!
Compatibility re-inflates
The final count follows the most complex station; G1 needs about 6 control points.
!
Untested
No test fixture yet.

## Slide 6
Where it lives
Simplify surface · gordonSurface
Draft 2026-09-26
Document | gordonSurface (d0950ed72a894fbe35c27d43)
Tab | simplifySurface
Tests | none yet
Examples | Test Part Studio 1: Simplify surface 1
Explainer | docs/explainers/gordon_surface/gordon_surface_explained.md, section 2.6
Related | Gordon Surface, Interior curves, Scaled Curve, Modify curve end, Pull surface, Simplify surface