## Slide 1
Create offset profile
Type an offset profile as regions or points -- width and height against station -- and get exact wires for Driven edge offset and Driven offset surface.
driven_offset (BeamBuilder Testbed) · Onshape custom feature
Draft 2026-09-29

## Slide 2
What it does
Create offset profile · driven_offset (BeamBuilder Testbed)
Draft 2026-09-29
Driven edge offset (DEO) and Driven offset surface (DOS) read an offset profile: wires in profile coordinates, X = station, Y = width offset, Z = height offset. Create offset profile builds those wires from a table, exactly (polynomial Beziers, no sampling), instead of a hand-drawn sketch.
Use it when
The offset is defined by regions: tip, running length, tail ...
Width or height ramps, holds or steps along X
Stations come from the part: a vertex or mate connector
Test T1: Tip w 0, RSL w 3, Tail w 0. The values jump at 0 and 1000, so the profile breaks there: three wires.

## Slide 3
Pieces and breaks
Create offset profile · driven_offset (BeamBuilder Testbed)
Draft 2026-09-29
A piece = one wire
A continuous stretch of the profile, e.g. T4 left: three Smooth points, one piece. Touching regions with equal values join too.
A break
Where the offset jumps (touching regions or two points at one station, different values -- T5 right) or is undefined (a gap in X), the profile ends and a new piece starts.
Ends
The profile starts at the first item and stops at the last; nothing is extrapolated.

## Slide 4
Region shapes
Create offset profile · driven_offset (BeamBuilder Testbed)
Draft 2026-09-29
Constant / Linear
One width and height; or a straight change from start to end values (corners at the ends).
Smooth
Smootherstep: flat, zero curvature at both ends of the change, never overshoots. Buffers hold the end values first (shaded).
Quadratic
A parabola flat at one end ('Flat at' Start or End), a kink at the other. Width and height use the same shape.

## Slide 5
Blending two regions
Create offset profile · driven_offset (BeamBuilder Testbed)
Draft 2026-09-29
Intersections
One entry per pair of consecutive regions, kept by region names. Blend off: join as they are if the values match, else break.
Blend on
A Hermite bridge from a distance into the first region to a distance into the second, G0 / G1 / G2 at each side.
Drag arrows
Each blend distance also has a drag arrow on the profile while the dialog is open.

## Slide 6
The dialog: Regions (1/2)
Create offset profile · driven_offset (BeamBuilder Testbed)
Draft 2026-09-29
1
2
3
4
5
# | Parameter | What it means
1 | Mode | Regions or Points.
2 | Region name | Empty = Region n. Intersections are kept by these names, so they must differ.
3 | Start station | Enter X (type the station) or At point.
4 | Start point | At point: a vertex or mate connector (one can be created in the field).
5 | Start offset along X | Station = the point's world X plus this signed distance.

## Slide 7
The dialog: Regions (2/2)
Create offset profile · driven_offset (BeamBuilder Testbed)
Draft 2026-09-29
6
7
8
9
# | Parameter | What it means
6 | End station | The same for the end. A region may be entered toward -X (start > end).
7 | Shape | Constant, Linear, Smooth or Quadratic.
8 | Start / end width, height | The values at each end (Constant: one Width, one Height).
9 | Intersections | Between consecutive regions, rebuilt automatically (next slides).

## Slide 8
The dialog: Quadratic and buffers
Create offset profile · driven_offset (BeamBuilder Testbed)
Draft 2026-09-29
1
2
3
4
# | Parameter | What it means
1 | Shape | Quadratic (test T8).
2 | Flat at | Start or End: the end of the change with zero slope; the other end meets its neighbour at a kink.
3 | Start / end width, height | End values; width and height follow the same shape.
4 | Start / end buffer | Hold the start (end) value this far in from that end; the change runs between the buffers. Not for Constant.
Entered toward -X, each end keeps its own values and buffer, and a quadratic's flat end stays at the end it was given (T11).

## Slide 9
The dialog: an intersection blend (1/2)
Create offset profile · driven_offset (BeamBuilder Testbed)
Draft 2026-09-29
1
2
3
# | Parameter | What it means
1 | Intersections | One per consecutive pair (here A / B), labelled by the region names.
2 | Blend | Off: touching regions with equal values join, anything else breaks. On: a blend.
3 | Continuity with first region | G0, G1 (tangent) or G2 (curvature) where the blend leaves region A.

## Slide 10
The dialog: an intersection blend (2/2)
Create offset profile · driven_offset (BeamBuilder Testbed)
Draft 2026-09-29
4
5
6
# | Parameter | What it means
4 | Distance into first region | How far back from A's end the blend starts.
5 | Continuity with second region | The same where it joins region B.
6 | Distance into second region | How far past B's start it ends. Both 0 only works across a gap in X.

## Slide 11
The dialog: Points
Create offset profile · driven_offset (BeamBuilder Testbed)
Draft 2026-09-29
1
2
3
4
5
6
# | Parameter | What it means
1 | Mode | Points: the profile through a list of stations.
2 | Station | Enter X or At point (vertex / mate connector plus a signed offset along +X).
3 | X | The station, typed.
4 | Width | Width offset at this station.
5 | Height | Height offset at this station.
6 | To next point | Smooth (flat at both points, no overshoot), Linear, or Hold (keep this value to the next point, then break). Ignored on the last point.
Two points at one station with different values are a jump: the profile breaks there (T5).

## Slide 12
Example: regions entered toward -X (T10, T12)
Create offset profile · driven_offset (BeamBuilder Testbed)
Draft 2026-09-29
For a part whose tip is at +X, enter regions from the tip: start 10100, end 10000. The same region stated low to high.
T10: Linear w 0 -> 4 with a start buffer of 20: width 0 held from 10100 to 10080, 4 at 10000. T12: two touching regions both entered toward -X join into one piece (w 1 at 12150, 2 at 12050).

## Slide 13
Driven edge offset takes regions directly
Create offset profile · driven_offset (BeamBuilder Testbed)
Draft 2026-09-29
Profile source: Regions
Driven edge offset has the same Regions table (same parameters, from offset_profile_core); no wire is made. Tests D1-D5: identical to the wire, within 1e-3 mm.
Stations
A region's X means what a wire's X means under DEO's Measure along. 'At point' stations land exactly on the part only when measuring along World X.
Not built yet
Per-break None / Line join in DEO / DOS. Today every break splits the output (D3: two offset bodies at the step).

## Slide 14
Outputs and messages
Create offset profile · driven_offset (BeamBuilder Testbed)
Draft 2026-09-29
Published for Extract variables
Key | What it holds
output | All piece wires (T1: 3).
piece1 .. pieceN | Each piece, in station order.
startVertex / endVertex | Where the profile starts (lowest station) / ends (highest).
breakVertices | The piece ends on both sides of every break (T1: 4).
pieceCount, breakCount | Numbers (T1: 3 and 2).
breakStations | Station of each break: a jump, or the middle of a gap (T1: 0, 1000 mm).
startStation, endStation | First and last station (T1: -100, 1100 mm).
Messages
 | Message / what to do
Error | Add at least one region. / Add at least two points at different stations.
Error | Regions 'A' and 'B' overlap. Regions may touch, not overlap.
Error | Region 'x': the buffers are as long as the region or longer.
Error | Two regions are named 'x' ... Intersections are kept by name.
Error | The blend between 'A' and 'B' has no length but the offset jumps ... Give a distance, or leave a gap in X.
Error | Start point: pick a point (vertex or mate connector) for the station. At point with nothing picked.

## Slide 15
Tips and limits
Create offset profile · driven_offset (BeamBuilder Testbed)
Draft 2026-09-29
✓
Name regions by role
Tip, RSL, Tail ... Intersection settings follow the names when regions are reordered.
✓
Smooth for joins that must not kink
A buffer into a Smooth ramp is curvature-continuous (C2); a Linear corner is only G0.
✓
Print segments
Debug group: every piece and sub-segment with its stations, degree and end values.
!
Breaks split the output
DEO / DOS have no per-break None / Line choice yet: a step in the profile is a step (a gap) in the offset.
!
One shape per region
Width and height share the region's shape.
!
Stations are world X
Picked points give their world X; on a part measured along its reference, place stations accordingly.

## Slide 16
Where it lives
Create offset profile · driven_offset (BeamBuilder Testbed)
Draft 2026-09-29
Document | driven_offset / BeamBuilder Testbed (f61d2c000ab2d1240776342e)
Tabs | create_offset_profile (the feature), offset_profile_core (regions / points -> exact pieces; shared with Driven edge offset)
Tests | Offset profile tests studio: T1-T12 (+ 3 error cases) -- devtools/onshape/build_offset_profile_tests.py, check_offset_profile.py; DEO regions tests: D1-D5 (5/5 pass 2026-09-29)
Design | driven_offset/research_create_offset_profile.md; driven_offset/DOCUMENT_MAP.md
Related | Driven edge offset, Driven offset surface (consumers); Evaluate offset (a profile measured from existing edges)